# Multiboard by Espablo
Supla for ESP8266 Firmware v2.7.2
Description https://forum.supla.org/viewtopic.php?f=11&t=3843
GPIO Button and Sensor should have a 4.7k pull-up to 3.3V VCC

Supported modules:
- ElectroDragon,
GPIO0 - Button1
GPIO2 - Button2
GPIO0 - Button Configure (5s)
GPIO16 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
GPIO4 - User Configurable
GPIO5 - User Configurable
GPIO14 - User Configurable
GPIO15 - User Configurable
- inCan,
GPIO2 - Temperature
GPIO4 - Sensor1
GPIO16 - Sensor2
GPIO14 - Button1
GPIO12 - Button2
GPIO5 - Relay1
GPIO13 - Relay2
GPIO0 - Button Configure (5s)
GPIO4 - Input CFG (x10)
GPIO2 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
- inCan RollerShutter,
GPIO2 - Temperature
GPIO4 - Sensor1
GPIO16 - Sensor2
GPIO14 - Button1
GPIO12 - Button2
GPIO5 - Relay1
GPIO13 - Relay2
GPIO0 - Button Configure (5s)
GPIO4 - Input CFG (x10)
GPIO2 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
- Melink
GPIO5 - Button
GPIO4 - Relay
GPIO5 - Button Configure
GPIO12 - LED CFG
GPIO3 - User Configurable
GPIO13 - LED Relay
- Neo Coolcam,
GPIO13 - Button
GPIO12 - Relay
GPIO13 - Button Configure
GPIO4 - LED CFG
- RELAYS x9,
GPIO2 - Temperature
GPIO1 - Relay1
GPIO3 - Relay2
GPIO4 - Relay3
GPIO5 - Relay4
GPIO12 - Relay5
GPIO13 - Relay6
GPIO14 - Relay7
GPIO15 - Relay8 - this port must have LOW after enabling or resetting the module
GPIO16 - Relay9
GPIO0 - Button Configure (5s)
GPIO2 - LED CFG
- SENSORS x8,
GPIO2 - Temperature
GPIO4 - Sensor1
GPIO5 - Sensor2
GPIO16 - Sensor3
GPIO12 - Sensor4
GPIO13 - Sensor5
GPIO14 - Sensor6
GPIO3 - Sensor7
GPIO1 - Sensor8
GPIO0 - Button Configure (5s)
GPIO2 - LED CFG
- Shelly 1,
GPIO5 - Button
GPIO4 - Relay
GPIO5 - Button Configure (x10)
- Shelly 2,
GPIO12 - Button1
GPIO14 - Button2
GPIO4 - Relay1
GPIO5 - Relay2
GPIO12 - Button Configure (x10)
- Shelly 2 RollerShutter,
GPIO12 - Button1
GPIO14 - Button2
GPIO4 - Relay1
GPIO5 - Relay2
GPIO12 - Button Configure (x10)
- SONOFF BASIC,
GPIO1 - Temperature
GPIO0 - Button1
GPIO14 - Button2
GPIO12 - Relay
GPIO0 - Button Configure
GPIO13 - LED CFG
GPIO3 - User Configurable
- SONOFF DUAL R2,
GPIO0 - Button1
GPIO9 - Button2
GPIO12 - Relay1
GPIO5 - Relay2
GPIO10 - Button Configure
GPIO13 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
- SONOFF S2X - Sonoff S20, S22 and S26 Smart Socket,
GPIO0 - Button
GPIO12 - Relay
GPIO0 - Button Configure (5s/x10)
GPIO13 - LED CFG
GPIO1 - User Configurable
GPIO2 - User Configurable
GPIO3 - User Configurable
- SONOFF TH,
GPIO14 - Temperature
GPIO0 - Button1
GPIO1 - Button2
GPIO12 - Relay
GPIO0 - Button Configure
GPIO13 - LED CFG
GPIO3 - User Configurable
- SONOFF TOUCH,
GPIO2 - Temperature
GPIO0 - Button
GPIO12 - Relay
GPIO0 - Button Configure
GPIO13 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
GPIO5 - User Configurable
- SONOFF TOUCH DUAL,
GPIO2 - Temperature
GPIO0 - Button1
GPIO9 - Button2
GPIO12 - Relay1
GPIO5 - Relay2
GPIO0 - Button Configure (5s)
GPIO9 - Button Configure (5s)
GPIO13 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
- SONOFF TOUCH TRIPLE,
GPIO2 - Temperature
GPIO0 - Button1
GPIO9 - Button2
GPIO10 - Button3
GPIO12 - Relay1
GPIO5 - Relay2
GPIO4 - Relay3
GPIO0 - Button Configure (5s)
GPIO13 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
- SONOFF_4CH,
GPIO2 - Temperature
GPIO0 - Button1
GPIO9 - Button2
GPIO10 - Button3
GPIO14 - Button4
GPIO12 - Relay1
GPIO5 - Relay2
GPIO4 - Relay3
GPIO15 - Relay4
GPIO0 - Button Configure (x10)
GPIO13 - LED CFG
GPIO1 - User Configurable
GPIO3 - User Configurable
- Yunshan,
GPIO3 - Button
GPIO4 - Relay
GPIO5 - Sensor
GPIO0 - Button Configure (5s)
GPIO2 - LED CFG
GPIO1 - User Configurable
- YUNTONG_Smart,
GPIO12 - Button
GPIO4 - Relay
GPIO12 - Button Configure
GPIO15 - LED CFG
GPIO13 - LED Relay
GPIO5 - User Configurable

Initial parameters for "ESP Flash Download Tool":
CrystalFreq 26M
SPI SPEED 40MHz
FLASH MODE DOUT
BAUDRATE 115200

FLASH SIZE 8Mbit (1MByte)
multiboard_1024_dout_eagle.flash.bin-------->0x00000
multiboard_1024_dout_eagle.irom0text.bin---->0x40000